## Slide 1: Computational Geometry Graham Rhodes Senior Software Developer, Applied Research Associates, Inc.

## Slide 2: What is Computational Geometry?
Manipulation and interrogation of shapes
Examples:
  “What is the intersection of a line and a triangle mesh”
  “What is the minimum distance separating two objects”
  “Break a mesh into pieces”

## Slide 3: Typical Application in Games
Interrogation of Geometry
  Collision detection for physics
  Proximity triggers for game logic
  Pathfinding, visibility, and other AI operations
Manipulation of geometry
  Creation of game assets in 3ds max/Maya/etc
  User-generated content (e.g., Little Big Planet)
  Destruction (Bad Company 2, etc., etc.)
Notes: A key takeaway for this talk is that geometry manipulation is no longer reserved for studio artists while producing a game. Geometry is generated and modified at runtime now, and the possibilities to explore this are wide open. There are good ways and bad ways to implement features in games that change the geometry of level and actor geometry. I want to introduce some good practices to game engine programmers working on these types of features, and perhaps to people who are looking to create their own geometry editors.

## Slide 4: Some Perspective
Game levels are usually made of meshes
  Typically made of triangles
  Indexed triangle meshes
X
Z
Y

## Slide 5: Some Perspective
Game levels are usually made of meshes
  Typically made of triangles
  Indexed triangle meshes
0 | <-.5, 0, 0>
1 | <0, 0, 0>
2 | <-.5, 0, .5>
3 | <0, 0, .5>
4 | <-.25, 0, 1>
5 | <-.5, 1, 0>
6 | <0, 1, 0>
7 | <-.5, 1, .5>
8 | <0, 1, .5>
9 | <-.25, 1, 1>
0
1
2
3
4
6
8
9

## Slide 6: Some Perspective
Game levels are usually made of meshes
  Typically made of triangles
  Indexed triangle meshes
0
1
2
3
4
6
8
9
0 | <-.5, 0, 0>
1 | <0, 0, 0>
2 | <-.5, 0, .5>
3 | <0, 0, .5>
4 | <-.25, 0, 1>
5 | <-.5, 1, 0>
6 | <0, 1, 0>
7 | <-.5, 1, .5>
8 | <0, 1, .5>
9 | <-.25, 1, 1>
Triangle Indices
0, 1, 2
1, 3, 2
2, 3, 4
1, 6, 3
3, 6, 8
3, 8, 9
3, 9, 4
…

## Slide 7: Some Perspective
Game levels are usually made of meshes
  Typically made of triangles
  Indexed triangle meshes
0
1
2
3
4
6
8
9
Triangle Indices
0, 1, 2
1, 3, 2
2, 3, 4
1, 6, 3
3, 6, 8
3, 8, 9
3, 9, 4
…
0 | <-.5, 0, 0>
1 | <0, 0, 0>
2 | <-.5, 0, .5>
3 | <0, 0, .5>
4 | <-.25, 0, 1>
5 | <-.5, 1, 0>
6 | <0, 1, 0>
7 | <-.5, 1, .5>
8 | <0, 1, .5>
9 | <-.25, 1, 1>

## Slide 8: Getting Ready
Computational geometry requires appropriate data structures
Notes: Those linear and indexed buffer representations are optimal for GPU operations (especially if optimally arranged for cache coherence, etc.), but not for general manipulation of geometry.

## Slide 9: Categories of Data Structures
Spatial
  Find things fast
  BSP tree, octree, Kd-tree, spatial hashing
  Etc…
Geometry + topology
  Change the shape of objects
  Focus of this talk!

## Slide 10: A Computational Geometry Problem
How?
We have polygons in our game level
The graphics card requires triangles
  Triangulation converts polygons into triangles

## Slide 11: The Polygon Triangulation Problem
Intuitive approach: ear-clipping
Fast approach: monotone decomposition
Both involve chopping triangles off in a sequence
Number of Polygons:
1
Polygon Indices
6,1,3,0,4,2,5
0
4
2
5
6
1
3
Notes: Monotone decomposition via plane sweep.

## Slide 12: The Polygon Triangulation Problem
Intuitive approach: ear-clipping
Fast approach: monotone decomposition
Both involve chopping triangles off in a sequence
0
4
2
5
6
1
3
Number of Polygons:
2
Polygon Indices
6,1,3,4,2,5
0,4,3

## Slide 13: The Polygon Triangulation Problem
Intuitive approach: ear-clipping
Fast approach: monotone decomposition
Both involve chopping triangles off in a sequence
0
4
2
5
6
1
3
Number of Polygons:
3
Polygon Indices
6,1,4,2,5
0,4,3
4,1,3

## Slide 14: The Polygon Triangulation Problem
Intuitive approach: ear-clipping
Fast approach: monotone decomposition
Both involve chopping triangles off in a sequence
0
4
2
5
6
1
3
Number of Polygons:
4
Polygon Indices
6,1,2,5
0,4,3
4,1,3
4,2,1

## Slide 15: The Polygon Triangulation Problem
Intuitive approach: ear-clipping
Fast approach: monotone decomposition
Both involve chopping triangles off in a sequence
0
4
2
5
6
1
3
Number of Polygons:
5
Polygon Indices
6,2,5
0,4,3
4,1,3
4,2,1
2,6,1

## Slide 16: The Polygon Triangulation Problem
Intuitive approach: ear-clipping
Fast approach: monotone decomposition
Both involve chopping triangles off in a sequence
0
4
2
5
6
1
3
Number of Polygons:
5
Polygon Indices
6,2,5
0,4,3
4,1,3
4,2,1
2,6,1

## Slide 17: The Polygon Triangulation Problem
Was maintaining the index list convenient?
NO!
  Original polygon: 6,1,3,0,4,2,5
  Final polygon: 2,5,6
  All the removed points were in the middle of the list!
  Maintaining the list can be error prone, and slow for complex models
  Inelegant

## Slide 18: Getting Ready
Computational geometry requires appropriate data structures!
(Lets take a look at one)
Triangulation Demo Part 1

## Slide 19: Geometric Model Representation
Geometry describes the shape of model elements (triangles)
Topology describes how the elements are connected

## Slide 20: Manifold Topology
Each edge joins exactly two faces
  Model is watertight
Open edges that join to one face are allowed
Modeling operation consistency rules
  “Invariants”
Non-manifold
Topology
Notes: This is our focus. Simple models with at most two triangles/polygons touching on common edges.

## Slide 21: Topological Data Structures
Enable elegant and fast traversals
  “Which edges surround a polygon?”
  “Which polygons surround this vertex?”
Easy to modify geometry
  Split an edge or face to add a new vertex
  Collapse an edge to simplify a mesh
Notes: The half edge structure we’ll talk about here enables many traversals that complete in linear time, based on the number of results retrieved.

## Slide 22: Other Topological Data Structures
Manifold
  Winged Edge (Baumgart, 1972)
  Half Edge (presented here)
  Quad edge
Non-manifold
  Radial edge
  Generalized non-manifold
Notes: Generalized non-manifold is the type of data structure used in computer aided design software. It completely separates geometry and topology, and is much more rigorous that what we need to be concerned with for games. It is also far more difficult to implement. The complete division between geometry and topology makes this quite non-intuitive.

## Slide 23: Half Edge Data Structure (HDS)
Basic topological element is a half edge (HE)
Geometry is implied by connections*
HE
Half Edge Properties

## Slide 24: Half Edge Data Structure (HDS)
HE connects a Start point to an End point
Traversal is StartPt to EndPt (edge is oriented)
Geometry is a straight
StartPt
EndPt
Half Edge Properties
EndPt
HE
Notes: The half edge only directly knows about its endpoint, but we’ll see that we can get to the start point in constant time.

## Slide 25: Half Edge Data Structure (HDS)
HE points to next half edge in traversal direction
Start point of HE.next is HE.EndPt
HE.next
Half Edge Properties
EndPt
Next
HE

## Slide 26: Half Edge Data Structure (HEDS)
Traversal directions are consistent
HE.next
HE.next.next
Half Edge Properties
EndPt
Next
HE

## Slide 27: Half Edge Data Structure (HEDS)
Note that sequence of half edges forms a loop!
So far, we only connect points (no polygons yet!)
Geometry is a wire
HE.next
HE.next.next
Half Edge Properties
EndPt
Next
HE

## Slide 28: Half Edge Data Structure (HEDS)
HE may point to a face on its left side
All half edges in a loop point to same face
Half Edge Properties
EndPt
Next
Face
HE
Face
Notes: The truth is, the face is on the left side only depending on viewpoint. If we look at the half edge from a point-of-view where the loop is traversed in a counterclockwise fashion, the face is on the left of the edge….while walking along the edge we would turn towards the left to see the face. If we looked at this same object from behind, the face would appear to be on the right.

## Slide 29: Half Edge Data Structure (HEDS)
HE points to its opposite half edge
Which is attributed as above
Half Edge Properties
EndPt
Next
Face
Opposite
Opposite

## Slide 30: Half Edge Data Structure (HEDS)
It is useful to store user data and a marker
Half Edge Properties
EndPt
Next
Face
Opposite
UserData
Marker

## Slide 31: Simple C++ HDS class definition
struct HalfEdge
{
HalfEdgeVert *endPt;
HalfEdge *next;
HalfEdge *opposite;
HalfEdgeFace *face;
void *userData;
unsigned char marker;
};
struct HalfEdgeVert
{
HalfEdge *halfEdge;
int index;
unsigned char marker;
};
struct HalfEdgeFace
{
HalfEdge *halfEdge;
unsigned char marker;
};
Notes: We are focusing on the half edge, but typical implementations also define special face and vertex data structures. These enable additional traversals that are useful.
The user data could be assigned to the edge, face, and/or vertex. It could store, for example, texture or UV mapping information.
The marker is useful to aid in traversals. For example, if you want to find he constellation of faces around a given starting face, then traverse around the face’s loop. For each vertex around the face, find the ring of faces around that vert, but skip any face that has a marker value of 1. For any as-yet-unmarked face, add it to your list, then set marker = 1 for that face. By using the marker in this way, it indicates that you’ve already visited a face and so it is already in your output list. You can also use this for Boolean type searches. For example, if you want to find faces connected to vert1, but not to vert2, first find the ring of faces around vert2, and set marker to 1. Then find the ring of faces around vert1, skipping any face with marker == 1. These are simple examples, but it should be clear that marker can enable rather complex selection logic.

## Slide 32: HDS Invariants
Strict
  halfEdge != halfEdge->opposite
  halfEdge != halfEdge->next
  halfEdge == halfEdge->opposite->opposite
  startPt(halfEdge) == halfEdge->opposite->endPt
  There are a few others…
Convenience
  Vertex == Vertex->halfEdge->endPt

## Slide 33: Simple Traversals
Find vertex loop defined by a half edge
IndexList FindVertexLoop(HalfEdge *edge)
{
IndexList loop;
HalfEdge *curEdge = edge;
do {
loop.push_back(edge.endPt->index);
curEdge = curEdge->next;
} while (curEdge != edge);
return loop;
};
Triangulation Demo
Part 2

## Slide 34: Simple Traversals
Find vertex loop defined by a half edge
IndexList FindVertexLoop(HalfEdge *edge)
{
IndexList loop;
HalfEdge *curEdge = edge;
do {
loop.push_back(edge.endPt->index);
curEdge = curEdge->next;
} while (curEdge != edge);
return loop;
};
curEdge
next

## Slide 35: Simple Traversals
Find vertex loop defined by a half edge
IndexList FindVertexLoop(HalfEdge *edge)
{
IndexList loop;
HalfEdge *curEdge = edge;
do {
loop.push_back(edge.endPt->index);
curEdge = curEdge->next;
} while (curEdge != edge);
return loop;
};

## Slide 36: Simple Traversals
Find vertex loop defined by a half edge
IndexList FindVertexLoop(HalfEdge *edge)
{
IndexList loop;
HalfEdge *curEdge = edge;
do {
loop.push_back(edge.endPt->index);
curEdge = curEdge->next;
} while (curEdge != edge);
return loop;
};

## Slide 37: Simple Traversals
Find vertex loop defined by a half edge
IndexList FindVertexLoop(HalfEdge *edge)
{
IndexList loop;
HalfEdge *curEdge = edge;
do {
loop.push_back(edge.endPt->index);
curEdge = curEdge->next;
} while (curEdge != edge);
return loop;
};

## Slide 38: Simple Traversals
Find vertex loop defined by a half edge
IndexList FindVertexLoop(HalfEdge *edge)
{
IndexList loop;
HalfEdge *curEdge = edge;
do {
loop.push_back(edge.endPt->index);
curEdge = curEdge->next;
} while (curEdge != edge);
return loop;
};

## Slide 39: Simple Traversals
Find vertex loop defined by a half edge
IndexList FindVertexLoop(HalfEdge *edge)
{
IndexList loop;
HalfEdge *curEdge = edge;
do {
loop.push_back(edge.endPt->index);
curEdge = curEdge->next;
} while (curEdge != edge);
return loop;
};

## Slide 40: Simple Traversals
Find vertex loop defined by a half edge
IndexList FindVertexLoop(HalfEdge *edge)
{
IndexList loop;
HalfEdge *curEdge = edge;
do {
loop.push_back(edge.endPt->index);
curEdge = curEdge->next;
} while (curEdge != edge);
return loop;
};
Notes: Note that we add each new edge in constant time, so the net cost is O(n), where n is the number of edges in the loop.

## Slide 41: Simple Operations
Split a face
edge1
edge2
edge4
edge3
vert1
vert2
HalfEdge edge1 = vert1.halfEdge;
HalfEdge edge2 = edge1.next;
HalfEdge edge3 = vert2.halfEdge;
HalfEdge edge4 = edge3.next;
*See speaker notes below slide for an important consideration!
Notes: IMPORTANT NOTE: If the face is part of a mesh, then edge1 is not necessarily the only edge whose endPt is vert1. Similarly, edge3 is not necessarily the only edge whose endPt is vert2. So, in the case of splitting a face in a mesh, it may be necessary to traverse the ring of edges around vert1 (and vert2) to find the edge whose endPt is vert1 (vert2) and whose face is the face of interest.

## Slide 42: Simple Operations
Split a face
vert1
vert2
HalfEdge edge1 = vert1.halfEdge;
HalfEdge edge2 = edge1.next;
HalfEdge edge3 = vert2.halfEdge;
HalfEdge edge4 = edge3.next;
HalfEdge newEdge = new HalfEdge;
newEdge
edge1.next = newEdge;
newEdge.next = edge4;
newEdge.face = edge1.face;
newEdge.endPt = vert2;

## Slide 43: Simple Operations
Split a face
vert1
vert2
HalfEdge edge1 = vert1.halfEdge;
HalfEdge edge2 = edge1.next;
HalfEdge edge3 = vert2.halfEdge;
HalfEdge edge4 = edge3.next;
HalfEdge newEdge = new HalfEdge;
edge1.next = newEdge;
newEdge.next = edge4;
newEdge.face = edge1.face;
newEdge.endPt = vert2;
edge1.face.halfEdge = edge1;

## Slide 44: Simple Operations
Split a face
vert1
vert2
HalfEdge newEd2 = new HalfEdge;
newEd2
newEd2.next = edge2;
newEd2.endPt = vert1;
edge3.next = newEd2;
newEdge.opposite = newEd2;
newEd2.opposite = newEdge;

## Slide 45: Simple Operations
Split a face
vert1
vert2
newFace = new HalfEdgeFace
newFace.halfEdge = edge2;
HalfEdge *curEdge = edge2;
do {
curEdge->face = newFace;
curEdge = curEdge->next;
} while (curEdge != edge2);
newFace
Triangulation Demo
Part 3

## Slide 46: Related Operations
Cut off an ear/triangle
  Exactly same as split face
  Apply recursively to triangulate face
Insert auxiliary edge
  Connect inner and outer loops to support holes in faces

## Slide 47: What Else Can We Do?
Split a mesh in half with a cutting plane
  Step 1: Split edges that cross the plane
  Step 2: Split faces that share two split edges
  …

## Slide 48: Intersection of edge and plane
Plane equation
Line Equation
v1
v2
?

## Slide 49: Intersection of edge and plane
Solve for t
If t >= 0 and t <= 1
  Edge touches plane
v1
v2

## Slide 50: What Can We Do with a B-rep Mesh?
Split a mesh in half with a cutting plane
  Step 1: Split edges that cross the plane
    Use marker variables to tag affected geometry
      Aids in finding related entities

## Slide 51: What Can We Do with a B-rep Mesh?
Split a mesh in half with a cutting plane
  Step 2: Split faces that share two split edges
Edge Split Demo
Part 1

## Slide 52: Simple Operations
Split an edge
HalfEdge edge1;
HalfEdge edge2 = edge1.opposite;
edge1
edge2

## Slide 53: Simple Operations
Split an edge
HalfEdge edge1;
HalfEdge edge2 = edge1.opposite;
HalfEdge edge1_b = new HalfEdge;
edge1_b.EndPt = edge1.EndPt;
edge1_b.face = edge1.face;
edge1_b.next = edge1.next;
edge1.EndPt = splitVert;
edge1.next = edge1_b;
edge1_b.EndPt.halfEdge = edge1_b;
edge1
edge1_b
edge2

## Slide 54: Simple Operations
Split an edge
HalfEdge edge1;
HalfEdge edge2 = edge1.opposite;
HalfEdge edge1_b = new HalfEdge;
HalfEdge edge2_b = new HalfEdge;
edge2_b.EndPt = edge2.EndPt;
edge2_b.face = edge2.face;
edge2_b.next = edge2.next;
edge2.EndPt = splitVert;
edge2.next = edge2_b;
edge2_b.EndPt.halfEdge = edge2_b;
HalfEdge edge1_b = new HalfEdge;
edge2
edge2_b
edge1
edge1_b

## Slide 55: Simple Operations
Split an edge
HalfEdge edge1;
HalfEdge edge2 = edge1.opposite;
HalfEdge edge1_b = new HalfEdge;
HalfEdge edge2_b = new HalfEdge;
edge2_b.opposite = edge1;
edge2.opposite = edge1_b;
edge1_b.opposite = edge2;
edge1.opposite = edge2_b;
splitVert.halfEdge = edge1;
edge2
edge2_b
edge1
edge1_b

## Slide 56: Other Operations
Remove face(s)
  Delete HalfEdgeFaces and any related topology that is unused elsewhere
  Take care to properly RE-connect half edges/verts that are not on open boundary

## Slide 57: Other Operations
Unhook face(s)
  Same as remove faces but copies removed face and related to another object

## Slide 58: What Else Can We Do?
Split a mesh in half with a cutting plane
  Step 3: Remove or unhook faces on one side
  Step 4: Find and cover open boundary loops
  Step 5: Triangulate the remaining faces
Edge Split Demo
Part 2

## Slide 59: Pop Quiz!
Find the open boundary vertices!
d
IndexList Boundary;
Boundary =
FindVertexLoop(startEdge->opposite);
(But what if the boundary isn’t connected properly?)
*See speaker notes below slide for an important consideration!
Notes: Caution! If the outer edges weren’t connected properly to begin with, will have to traverse edge rings (see following slides) for each boundary vertex to locate the boundary edges from the inside. This is more expensive. Best to make sure the data structure is properly created and maintained, in order to extract the best performance.

## Slide 60: Simple Traversals
Find edges around a vertex
EdgeList FindEdgeRing(HalfEdgeVert *vert)
{
EdgeList ring;
HalfEdge *curEdge = vert->halfEdge;
do {
ring.push_back(curEdge);
curEdge = curEdge->next->opposite;
} while (curEdge != vert->halfEdge);
return ring;
};

## Slide 61: Simple Traversals
Find edges around a vertex
EdgeList FindEdgeRing(HalfEdgeVert *vert)
{
EdgeList ring;
HalfEdge *curEdge = vert->halfEdge;
do {
ring.push_back(curEdge);
curEdge = curEdge->next->opposite;
} while (curEdge != vert->halfEdge);
return ring;
};
next
opposite

## Slide 62: Simple Traversals
Find edges around a vertex
EdgeList FindEdgeRing(HalfEdgeVert *vert)
{
EdgeList ring;
HalfEdge *curEdge = vert->halfEdge;
do {
ring.push_back(curEdge);
curEdge = curEdge->next->opposite;
} while (curEdge != vert->halfEdge);
return ring;
};
Notes: Supposed you needed to find all faces connected to a collection of vertices
You can use the approach shown here to collect faces for each vertex
Use marker values to avoid collecting a given face more than once

## Slide 63: What Else Can We Do?
Generate a convex hull mesh
  Divide and conquer method is fast
    O(n log n)
Role of the half edge data structure
  Remove interior faces/edges during stitch phase
  Create new faces between boundary loops to perform the stitch

## Slide 64: What can go wrong?
Be careful when clipping concave face
  Clipping against a plane can generate multiple loops
  User marker flags to tag start and stop points
  Recursively traverse to find ears to clip

## Slide 65: What can go wrong?
Some scenarios produce multiple loops
  Holes in a face
  Requires additional triangulation logic
  Nested loops: auxiliary edge to convert to simple polygon
  Multiple un-nested loops: locate and triangulate each loop separately
*See speaker notes below slide for an important consideration!
Notes: NOTE: It is straightforward to triangulate/cover an open loop that is on a plane. Or one that is approximately planar. If the edges on the loop are not all coplanar, then it is trickier. It may be possible to find some projection plane in which to perform the triangulation connectivity (a plane in which the projection of the edge loop is a simple polygon with all the original edges visible), but a different triangulation will result from different project plane choices. Ultimately, the triangles produced will not be coplanar if the edges were not coplanar, of course.

## Slide 66: What can go wrong?
Tolerance issues
  Edges not quite collinear
    Location of intersection point is highly sensitive
  Points nearly collocated
    Possible creation of very short/degenerate edges
  On which side of an edge is a point?/Which face does a ray intersect?

## Slide 67
Orientation Inversion
Notes: This grid is a portion of the representable floating point numbers. These two triangles are defined by corners that are representable points. Points not lying on the intersection of horizontal and vertical grid lines are not representable. Any unrepresentable number is approximated by a representable number.

## Slide 68
Orientation Inversion
Notes: This intersection point is not representable, so the floating point math system will approximate it with the nearest representable number coordinate.

## Slide 69
Orientation Inversion

## Slide 70
Orientation Inversion

## Slide 71
Orientation Inversion
Polygon is no longer simple (it self-intersects) and no longer has a consistent orientation

## Slide 72
Cascades of Extraneous Intersections
Notes: Here, though the floating point grid is not shown, you will see that a single non-representable intersection point can lead to a chain of intersections that aren’t present in the original perfect geometry.

## Slide 73: Cascades of Extraneous Intersections

## Slide 74: Tolerant Geometry
Treat edges and points as thick primitives
  Assign a radius to be used in intersection and proximity testing
2
1
Is point on edge?
On left side?
On right side?
2
1
Point is ON the edge
Ambiguous answer depends on:
Edge from 1->2 or 2->1
Location

## Slide 75: References and Resources
Sample code for half edge data structure
  http://www.essentialmath.com
These slides
  See http://www.gdcvault.com after GDC
References
  http://www.cs.cornell.edu/courses/cs4620/2010fa/lectures/05meshes.pdf (Shirley & Marschner)
  http://www.cgafaq.info/wiki/Half_edge_general
    Nice discussion of invariants
  http://people.csail.mit.edu/indyk/6.838-old/handouts/lec4.pdf
    Polygon triangulation

## Slide 76: References and Resources
More references
  Tolerant geometry and precision issues
    Christer Ericson, Real-time Collision Detection
    Jonathan Shewchuk’s, “Adaptive Precision Floating-Point Arithmetic and Fast Robust Predicates for Computational Geometry”
    John Hobby, “Practical Segment Intersection with Finite Precision Output” (snap rounding)

## Slide 77: Questions?